## Slide 1: Building a Personal Computer
Presented By: Jeffrey S. Walley
CTEC-112 IT Hardware Support
Fall 2022

## Slide 2: Use Cases for the PC
School work
Office and Productivity
Digital Art
Gaming
Virtualization
Docker
Web browsing & Entertainment

## Slide 3: Build Budget
I am looking to spend $1200 on this PC Build.

## Slide 4: MOTHERBOARD: MSI MAG B550 Tomahawk
AMD AM4 Socket
Full sized ATX
6GB/s SATA
USB 3.2
1G & 2.5G LAN RJ-45
Dual M.2 22.80 & 22x110
DD4 with Memory Boost

## Slide 5: Desktop PC Case
Fractal Design
Pop xl atx
High-AirFlow
Full ATX Desktop
2x 5.25” bays
3x Storage trays
  3.5” & 2.5” / tray
Front I/O:
  2x USB 3.0
  Headphone / Mic
  Power / Reset
Increased Airflow

## Slide 6: Central Processor Unit
AMD Ryzen 7 5800x
  8 Core / 16 Thread
3.8 GHz / up to 4.7 GHz
7nm Vermeer Zen 3
32MB L3 / 4MB L2 Cache
TDP 105W

## Slide 7: PC Memory (RAM)
G-Skill Ripjaw v
32GB (2x 16GB)
DDR4 SDRAM 3200
PC4-25600
Timing: 16-18-18-38

## Slide 8: Cooling Unit
4 Heat Pipes Direct Contact
Nickle Black Fins
Brushed Aluminum Surface
42 CFM Airflow
Noise Level: 26.0 dBA

## Slide 9: Power Supply (PSU)
Corsair RM850
850 Watt
Low Noise
Modular Connectors
Gold Efficiency Rating

## Slide 10: Storage Device 01- C:
OS – SSD
  Western Digital Black SN850
    500GB
      7000 MB/s read
      5300 MB/s write
    NVME / M.2 2280
    PCIe 4.0

## Slide 11: Storage Device 02- S:
Toshiba x300
6TB
7200 RPM
256 MB Cache
6Gb/s SATA 3
  Application Data
  Virtual Machines
  Images
  Movies & Music
  Games

## Slide 12: Video Card (GPU) GIGABYTE Radeon RX 6600
    AMD Radeon 6600
    8GB 128-bit GDDR6
    PCIe 4.0
  1792 Stream Processors
  28 Ray Accelerators
    2491MHz Boost

## Slide 13: Monitor
MSI Optix G27c4 27”
Curved Monitor
27” Curved Display
1920 x 1080
170 Hz Refresh Rate
1ms Response Time
AMD Freesync
Wide Color Gamut
Frameless Design
Purchasing 2 for dual Monitor setup

## Slide 14: Operating System & Additional Apps
Ubuntu OS
LibreOffice
Krita (for Digital Art)
GIMP (for Digital Photography)
VMWare Workstation Pro (Virtualization)
Docker (Container Deployment)
+ Steam, Epic and GoG for Gaming
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 15: Final Budget
Motherboard:
  MSI B550 Tomahawk $169.99
PC Case:
  Fractal Pop XL Black $109.99
Processor:
  AMD Ryzen 7 5800x 8-core $248.00
RAM:
  G.SKILL Ripjaw V Series 32 GB $89.78
Cooling:
  Cooler Master Hyper 212 Black $54.99
Power Supply:
  Corsair RM850 850 Watt $114.99
SSD:
  Western Digital Black SN850 500 GB $69.99
HDD:
  Toshiba X300 6 TB $144.99
Video Card
  GIGABYTE Radeon RX 6600 $219.99
Monitor
  2x MSI Optix 27” Curved $399.98
OS & Additional Software: FREE
Subtotal from NewEgg $1622.69

## Slide 16: Conclusion:
In this project I attempt to build a computer for Productivity, Virtualization, Entertainment, and Gaming for $1200. I chose a MSI B550 Tomahawk Motherboard with an 8-core AMD Ryzen 7 5800x CPU as the brains of the computer. The computer will feature a Cooler Master Hyper 212 CPU cooler and a Fractal Design Pop XL Air Full ATX case, for easy future upgrading. It will feature 32 GB of G.Skill DDR4 3200 RAM, along with a 500 GB SSD drive for the OS, and 6 TB of HDD for applications, data storage, and games. The video card will be a Radeon RX 6600 with 8Gb of GDDR6 memory.
If I had stopped with the initial build, I would have successfully built the Desktop for a subtotal of slightly more than $1200, pre-Black Friday / Cyber-Monday deals. I added 2 monitors for a dual monitor setup and ended up spending another $400. The subtotal with the monitors is $1622.69 on the Newegg.com website. I will end up adding a mechanical keyboard and triple monitor mount to bring the subtotal up to $1900 or more eventually.
I currently have 2 monitors and multiple keyboards and mice, so I can successfully build the desktop for a price within my budget (excluding Tax and Shipping). If I am to build this system, I will wait until Black Friday or Cyber Monday when many of these parts will be discounted.